## Slide 1
F. ORDÓÑEZ
C. CALIOT
G. LAURIAT
F. BATAILLE
Étude paramétrique et optimisation d’un récepteur solaire à particules

## Slide 2
Summary
Context
Objectives
Physical model
Results
Conclusions and future works
2

## Slide 3
Cost of energy production 129-206 $/MWh 74-102 $/MWh
Annual net efficiency 12-20 % > 50%
Source: Romero et al. 2000
Source: Lazard estimates 2009
Solar Thermal Power Plants Gas Combined Cycle
Increasing the cycle efficiency.
Increasing the temperature of working fluid.
3
Notes: 1. Nowadays, the annual global efficiency of Solar Thermal Power Plants is lesser than 20% face to gas combined cycle efficiency which is around 50%

## Slide 4
Source: Romero et al. 2002
In tube receivers the solar radiation is absorbed in surface
In volumetric receiver the solar radiation is absorbed into the volume
4

## Slide 5
Source: Karni and Bertocchi 2005
Ceramic foam (SiC)
Two concepts of volumetric receivers exist
Porous receivers
Particles receivers
Source: Wu et al. 2011
5

## Slide 6
Volumetric receivers seeded by particles
Particles: sub-micron carbon particles
Particle radius recommended: 0,2 µm
Temperature reported: 1000 K
Theoretical efficiency: 90%
Windowless atmospheric pressure receiver
Particles: sintered bauxite
Particle diameter: 0.7 mm
The particles serve themselves as storage medium
Theoretical efficiency: 89%
Source: Kitzmiller et al. 2012
Source: Gobereit et al. 2012
6

## Slide 7
Summary
Context
Objectives
Physical model
Results
Conclusions and future works
7

## Slide 8
This study has two main objectives:
  To build a simplified model of a solar receiver seeded by particles
  To optimize the parameters that drive the efficiency of solar particle receiver
Objectives
8
Design and modeling of a solar particle receiver optimized
Notes: 6. There is not enough information about the optimal values of parameters that drive the solar particle receiver behavior which allow maximizing its efficiency.

## Slide 9
Strategy
1 Parametric study for a single particle (n, k, r)
2 Parametric study for a slab of particles mono-disperses (n, k, r, fv)
4.1 Optimization of a slab of particles mono-disperses
4.2 Optimization of a slab of particles poly-disperses
9
3. Minimizing the Reflectance
Notes: 6. There is not enough information about the optimal values of parameters that drive the solar particle receiver behavior which allow maximizing its efficiency.

## Slide 10
Summary
Context
Objectives
Physical model
Results
Conclusions and future works
10

## Slide 11
Asymmetry parameter
Mie efficiencies
A simplified model has been developed (mono-dimensional and single layered geometry, cold media, poly-dispersion of spherical particles)
Model physique
The Lorenz-Mie theory has been used to found the radiative properties of particles (Mie efficiencies and asymmetry factor) and the Henyey-Greenstein phase function has been used to solve the angular behavior of scattering
11

## Slide 12
A simplified model has been developed (mono-dimensional and single layered geometry, cold media, poly-dispersion of spherical particles)
Volumetric coefficients
Model physique
Gamma distribution
12
Optical depth

## Slide 13
The radiative transfer equation (RTE) has been solved with a two-stream approximation
A simplified model has been developed (mono-dimensional and single layered geometry, cold media, poly-dispersion of spherical particles)
Forward and backward streams
Model physique
13

## Slide 14
A simplified model has been developed (mono-dimensional and single layered geometry, cold media, poly-dispersion of spherical particles)
Model physique
14
Intensity vs angle for a slab of particles mono-disperses at τ=2
m=2,7+0.8i
r=5 µm
τ0= 4
A modified Eddington-delta function hybrid method has been used to approximate the intensity (I)

## Slide 15
Summary
Context
Objectives
Physical model
Results
  Parametric study
  Receiver optimization
Conclusions and future works
15

## Slide 16
Scattering albedo
g=-1 g=0 g=1
ωt tends to one ωt tends to zero
Parametric study for a single particle
Parameters
refractive index: m=n+ik
particle radius: r
Transport albedo
λ=0.5 µm
16

## Slide 17
ωt vs k; n=2.27496 Qabs vs k; n=2.27496
Parametric study for a single particle
For k<0.01
x increases→ absorption increases →ωt decreases
For 0.01<k<0.5
absorption increases → ωt decreases
For k>0.5
absorption decreases → ωt increases
17

## Slide 18
The Reflectance has been taken as the indicator of efficiency receiver
Reflectance
Parametric study for a slab of particles mono-disperses
Parameters
refractive index: m=n+ik
particle radius: r
volumetric fraction: fv
λ=0.5 µm
18

## Slide 19
R vs k (n=2.27496 and fv=5e-6)
Parametric study for a slab of particles mono-disperses
For the same volume fraction, the slab of small particle contain more particles than the slab of large particles
For large particles one can minimizes the reflectance increasing the volume fraction
R vs fv (n=2.27496 and k=0.87417)
19

## Slide 20
Summary
Context
Objectives
Physical model
Results
  Parametric study
  Receiver optimization
Conclusions and future works
20

## Slide 21
Receiver optimization
A Particle Swarm Optimization (PSO) algorithm has been used to find the parameters that minimize the reflectance (R) for:
Slab of particles mono-disperses
Slab of particles poly-disperses
Parameters for slab of particles mono-disperses
refractive index: m=n+ik
particle radius: r
volumetric fraction: fv
21

## Slide 22
Receiver optimization
A Particle Swarm Optimization (PSO) algorithm has been used to find the parameters that minimize the reflectance (R) for:
Slab of particles mono-disperses
Slab of particles poly-disperses
Parameters for slab of particles poly-disperses
refractive index: m=n+ik
most probable radius: rmp
width parameter: rmp/r32
volumetric fraction: fv
22

## Slide 23
Receiver optimization
Slab of particles mono-disperses
Slab of particles poly-disperses
23
2,8.10-3
1,5
0,04
4,5
0,9
2,5.10-5
0,95
0,54
8
2,9.10-3
1,5
0,006
50
0,9
2,9.10-4
0,95
0,55
8
2,7.10-3
1,5
0,04
4,6
2,3.10-5
0,95
0,53
8
2,9.10-3
1,5
0,006
50
2,6.10-4
0,95
0,55
8

## Slide 24
Summary
Context
Objectives
Physical model
Results
Conclusions and future works
24

## Slide 25
An optimization of a solar particle receiver was done with the help of a PSO algorithm
A solar particle receiver was modeled as an absorbing, anisotropic scattering and cold media slab of particles (mono and poly disperses)
Conclusions
25

## Slide 26
1/ Improvement of the model for a slab of particles with absorption, scattering and emission.
3/ Optimization of this new model with the PSO algorithm developed.
2/ Development of a multi-slab model.
4/ Study of coupling of heat transfer between radiation and convection in a solar particle receiver optimized.
Future works
26

## Slide 27
Thanks for your attention

## Slide 28
q0/q0e-τ/µ0
q+/q0(τ0= 8)
q-/q0(τ0= 8)
q0/q0e-τ/µ0
q+/q0(τ0= 4)
q-/q0(τ0= 4)
Parametric study for a slab of particles
Radiative fluxes: collimated, forward diffuse and backward diffuse for two different optical ticknesses τ0 = 4 and τ0 = 8 (n=1.5, k=0,0425 and r=4.63 µm)
For these conditions the asymptotic reflectance is reached when the optical thicknesses is 8